## Slide 1
C1 Basic concepts for hazard communication
Campus Occupational Safety and Health knowledge and education training promotion program of the Ministry of Education

## Slide 2
Notices for use of the teaching material
Copyright of the slides of the teaching material (including text and image files) belongs to the ministry.
Core teachers: Any slide in the teaching material should be employed in full in teaching, without arbitrary revision and editing.
Credit is required for use of the material as reference in teaching.

## Slide 3: Contents
  I. Introduction
  II. Development of Taiwan's communication system for chemical hazards
  III. Purpose of hazard communication
  IV. What are hazardous chemicals (hazardous materials)
  V. Regulations for the Labeling and Hazard Communication of Hazardous Chemicals

## Slide 4
In line with the UN regulation of labeling of chemicals, article 7 of Taiwan's Occupational Safety and Health Act stipulates that employers should label dangerous and hazardous substances and highlight necessary safety and health notices. In 1992, the Council of Labor Affairs (forerunner of the Ministry of Labor) promulgated "Regulations of Hazard Communication on Dangerous and Harmful Materials.“
I. Introduction

## Slide 5
After having successfully ironed out differences among some countries concerning classification and labeling of chemicals, the United Nations publicized Global Harmonized System (GHS) in 2002, calling for implementation by countries around the world by 2008.
I. Introduction

## Slide 6
Accordingly, Taiwan has revised CNS6864 on symbols for the transport of dangerous goods (keeping nine categories, only applicable to the transportation industry) and formulated CNS 15030 "standards for classification and labeling of chemicals," according to the UN GHS Purple Book, which divides chemicals into 27 kinds under three categories, including 26 kinds under two categories of chemicals in workplaces and one kind under one category involving environmental hazard.
I. Introduction

## Slide 7
Subsequently, the Council of Labor Affairs formulated "Regulations of Hazard Communication on Dangerous and Harmful Materials," renamed as "Regulations of Hazard Communication on Hazardous Chemicals" by its successor the Ministry of Labor on July 3, 2014.
I. Introduction

## Slide 8
Promulgation of "Labor Safety and Health Act" on April 16, 1974.
Revision of "Labor Safety and Health Act" on May 17, 1991, with addition of article 7.
Formulation of "Regulations of Hazard Communication on Dangerous and Harmful Materials" on Dec. 28, 1992.
Revision of "Regulations of Hazard Communication on Dangerous and Harmful Materials," changing MSDS to 16 items on Jun. 29, 1999
II. Development of Taiwan's hazard communication system for chemicals

## Slide 9
Formulation of "Regulations for the Labeling and Hazard Communication of Dangerous and Harmful Materials" on Oc. 19, 2007 (in compliance with the preliminary norms of GHS).
Implementation of GHS on Dec. 31, 2008, in line with the resolutions of the United Nations and APEC.
Implementation of "Regulations of Hazard Communication on Hazardous Chemicals" on July 3, 2014.
II. Development of Taiwan's hazard communication system for chemicals

## Slide 10
Original hazard communication system:
Categorization: nine categories
Basis of labeling: CNS6864 and UN Orange Book, or UN Recommendations on the Transport of Dangerous Goods Model Regulations
Consistent labeling between transport and workplaces
MSDS covers contents of 16 items.
Original hazard communication system
& GHS
GHS:
Categorization: 27 kinds under three major categories
Basis of labeling: CNS15030 and the UN GHS Purple Book
Labeling inconsistent between transport and workplaces but more inclusive
No much change in substantial contents, with SDS still covering 16 items.

## Slide 11
Hazard recognition: Help laborers recognize potential hazards in workplaces.
Laborers' right to know: Laborers have the right to know potential hazards for substances they contact in workplaces.
Reduction of hazards: Consensus forms between employers and laborers, thereby cutting hazards.
III. Purposes of hazard communication

## Slide 12: IV. What are hazardous chemicals (hazardous materials)
Hazardous materials
dangerous materials
harmful materials
What are dangerous materials?
What are harmful materials?
Materials that may cause the dangers of burning and explosion.
Materials that may cause poisoning or harm health.
Dangerous materials and harmful materials monitored and controlled by the Council of Labor Affairs
Toxic chemicals monitored and controlled by the Environmental Protection Administration
(305 kinds in four categories)
Dangerous materials monitored and controlled by Ministry of Transportation and Communications (nine major categories)

## Slide 13: V. Regulations for the Labeling and Hazard Communication of Hazardous Chemicals
Chapter 1 General principles
Chapter 2 Labeling
Chapter 3 Safety data sheet, checklist, disclosure, and communication measures
Chapter 4 Supplementary provisions

## Slide 14
Produce checklist of hazardous materials.
Provide safety data sheet (SDS).
Place label on containers (hazard symbol + contents)
Provide employees education and training on hazard communication (three hours).
Formulate hazard communication plan.
Five major mandatory work items for employers

## Slide 15
Chapter 1 Hazardous chemicals
in workplaces (26 kinds)
Physical hazards (16 kinds) | Health hazards (10 kinds)
Explosives Inflammable gas Inflammable aerosol Oxidizing gas Pressurized gas Inflammable liquid Inflammable solid Self-reaction substances Pyrophoric liquid Pyrophoric solid Substances forbidden to contact with water Oxidizing liquid Oxidizing solid Organic peroxide Metal corrosive | acute toxins: swallowing, skin, inhalation Corrosive/skin-irritating substances Substances seriously damaging/irritating eyes Allergens for respiratory tract or skin Mutable substances for reproductive cells Carcinogen Reproductive toxin Toxin for specific organ system -- Single exposure Toxin for specific organ system --Multiple exposure Inhalation hazardous substance

## Slide 16
Labeling items:
1) Hazard symbol 2) Contents
Labeling regulations:
Containers containing over 100 ml hazardous chemicals should bear label according to the classification and symbol set in the regulation (for chemicals unable to be classified, label with contents only is sufficient), with description of contents mainly in Chinese, supplemented with some foreign language understandable to laborers handling operation, if necessary.
For containers with capacity less than 100 ml, labeling only needs to include chemical name, symbol, and word of warning.
Chapter 2 Labeling

## Slide 17
Types of hazard symbols (1)
Exclamation mark
Corrosion
Flame
Inflammable substances
Pyrophoric substances
Substances forbidden to contact with water
Organic peroxide
Metal corrosive
Corrosion/grade-1 irritant
Grade-4 acute toxin
Corrosion/grade-2 irritant

## Slide 18
Health hazard
Gas cylinder
Flame atop a circle
Oxidizing gas
Oxidizing liquid
Oxidizing solid
Pressurized gas
Carcinogen
Toxin
Inhalation hazardous substance
Types of hazard symbols (1) (cont.)

## Slide 19
Explosive
Self-reaction substances
Organic peroxide
Grade 1-3 acute toxins
Toxin for water environment
Bomb explosion
A skull and crossbones
Hazardous substances for environment
Types of hazard symbols (1) (cont.)

## Slide 20
Types of hazard symbols (2)
Physical hazards (five kinds)
Health hazards (five kinds)
Environmental hazard (one kind)

## Slide 21
Upright square at 45-degree angle
Large enough for clear identification
Black pattern, white background, in red frame with sufficient wide for warning function
45˚
Shape and size of symbols

## Slide 22
Flame→inflammable substance
Flame atop a circle→oxidizing substance
Bomb explosion→explosive
Corroded hand and metal→corrosive
Steel cylinder→pressurized gas
Skull→toxin
Exclamation mark→warning (low toxicity, low irritation) Human body→hazardous substance for health (including carcinogen)
Withered tree and dead fish→hazardous substance for environment
Significance of symbols

## Slide 23
1. Name：
Name of substance, common name and chemical name
2. Hazardous ingredients：
All the ingredients with physical hazard or health hazard
consisting of warning for danger and common warning, the former involving more serious hazard
3. Word of warning：
Contents of labeling

## Slide 24
Necessary preventive measures, such as
deposit in shaded cool area, keeping
containers sealed, avoiding contact with
skin, and wearing proper protective
equipment. Business units can produce
message by their own, since there are
no standard one
a rapid channel for inquiry by users, which can be exempted in case there is constant change in the information and SDS is available.
6. Name, address,
and telephone number
of manufacturer or
supplier：
0
4. Message for hazard warning：
Describe hazardous nature of substance in common language, such as gas with propensity to burn, fatal for ingestion.
5. Preventive measures for hazards：

## Slide 25
Hazard symbol, word of warning, hazard warning message should conform to regulations in table 1 in the appendix.
Health hazards which need labels of skull, corrosion, and respiratory-duct allergy don't need exclamation mark label.
When there are two or more labels, they should be juxtaposed in a clear manner arranged according the status of container.
In case word of warning contains both danger and common warning, label of danger will suffice.
Hazard warning message should be displayed in entirely
①
②
③
Labeling format

## Slide 26
Name: Benzene
Hazardous ingredient: Benzene
Word of warning: Danger
Hazard warning message: Highly inflammable liquid and vapor, inhalation hazard, irritant to skin, possible carcinogen
Preventive measures for hazard:
  Cap container tightly
  Deposit container in place with good ventilation
  Stay away from inflammable
  In case of contact with eyes, wash eyes with massive amount of water before seeking medical treatment.
  Don't pour the material into drainage.
Manufacturer or supplier:
  (1) Name: (2) Address: (3) Telephone No.:
* For more detail data, refer to the substance's safety data sheet.
Danger

## Slide 27
Internal-layer container as lining with external layer already bearing label
External container with internal-layer container with label visible from outside
Personal portable container of laborer containing hazardous substance retrieved from labeled container for use by laborers on duty.
Hazardous substance retrieved from labeled container for use in experiment and research in laboratory
Containers exempt from labeling

## Slide 28
Several containers containing similar hazardous substance placed in the same place
Ducting or piping system
Such chemical equipment as reactor, distillation tower, absorption tower, extractor, blender, precipitator, heat exchanger, measuring tank, or storage tank
Equipment such as cooling device, stirring device, or compression device
Conveying apparatus
Containers whose labels can be substituted by installation of bulletin board

## Slide 29
Chapter 3 Safety Data Sheet
Safety Data Sheet, SDS
ID of Chemicals
Instructions of Chemicals

## Slide 30
For hazardous chemicals, employer should provide laborers safety data sheet (mainly in Chinese) conforming to regulation in terms of content items and format.
For chemical which is a mixture of two or more hazardous ingredients, produce safety data sheet according to the hazard after mixture.
Employer should review and update the contents of safety data sheet to assure its correctness at least once every three years.
Record for upgrading of safety data sheet, including contents, date, and edition, should be kept for three years.
Employer cannot refuse requirement by competent authority, labor inspection institution or doctors, and first responders for the provision of safety data sheet and withholding information.
Notices for safety data sheet

## Slide 31
A. Data on chemicals and companies
Name of substance:
Other name:
Suggested usage and usage restriction
Name, address, and telephone number of manufacturer, importer, or supplier
Emergency contact phone number/fax number:
Purpose: Provide a rapid channel for inquiry, when user has question on contents of SDS or emergent accident occurs.

## Slide 32
Classification of chemical hazards:
Contents of labeling:
Other hazards
B. Data on hazard identification
Purpose: Enable user to have a rapid grip on the classification of chemical hazards and their effect

## Slide 33
Name in Chinese and English:
Synonym:
CAS No.:
Composition of hazardous ingredients (percentage):
C. Data on identification of ingredients
Purpose: Enable user to know name and composition of chemicals

## Slide 34
First aids for different kinds of exposures:
Major symptoms and hazard effect
Protection for first-aid providers
Suggestions to doctors
D. First aids
Purpose: Help first-aid providers and doctors take handling measures instantly following occurrence of disaster.

## Slide 35
Applicable fire-extinguishing agents:
Possible special hazards in fire fighting:
Special fire-fighting procedure
Special protective equipment for fire fighters:
E. Fire-fighting measures
Purpose: Minimize fire loss by providing information on applicable fire-fighting agents, procedure, and possible special hazards.

## Slide 36
Notices for individuals:
Notices for environment:
Cleaning method:
F. Leakage handling method
Purpose: Provide notices in handling chemical leading, so as to reduce adverse effect and damage on human life, properties, and environment.

## Slide 37
Disposal:
Storage
G. Safe disposal and storage method
Purpose: Provide user norm or guidance for disposal and storage of substance, to cut its potential hazard.

## Slide 38
Purpose: Provide user information on necessary engineering control countermeasure and personal protection equipment and measures,
in order to reduce exposure hazard, plus provision of control parameters, such as permissible exposure limit-ceiling.
Engineering control:
Control parameter: PEL-TWA, permissible exposure limit-time weighted average/PEL-STEL/PEL-C, permissible exposure limit-ceiling Biological indicator:
Personal protective equipment:
Health measures:
H. Preventive measures for exposure

## Slide 39
PEL-TWA | E.P. | Notes
Less than 1 | 3 | Permissible exposure for gaseous substance is based on the unit of ppm, granular material on mg/m3, asbestos on f/cc.
More than 1, less than 10 | 2 | 
More than 10, less than 100 | 1.5 | 
More than 100, less than 1,000 | 1.25 | 
More than 1,000 | 1 | 
Three kinds of permissible exposure limits
PEL-TWA: applicable to chronic hazardous substance.
PEL-STEK (15 minutes): applicable to chronic hazardous substance
  PEL-STEL(15Minutes)＝PEL-TWA× E.F
PEL-ceiling (PEL-C，for any time)：applicable to highly acute hazardous substance

## Slide 40
Purpose: To assist users to identify the physical and chemical properties of this substance, as a reference for normal operation and emergency response.
Appearance (substance, color) | Odor
Olfactory threshold | Fusion point
pH value: | Boiling point/boiling range
Flammability (solid, gas): | Flash point: ℉ ℃ Testing method: open cup closed cup
Decomposition temperature: | 
Self-ignition temperature: | Explosion limit:
Vapor pressure: | Vapor density:
Density: | Solubility:
Octanol/water partition coefficient (log Kow): | Evaporation rate:
I. Physical and chemical properties

## Slide 41
Stability:
Possible hazard reaction under special situation:
Status which should be avoided:
Substance which should avoided:
Hazardous decomposition products:
J. Stability and reactivity
Purpose: Provide data on reaction feature of substance, as reference for laborers or occupational safety and health workers in storage, transport, handling, or disposal of chemicals

## Slide 42
Exposure channel:
Symptoms:
Acute toxicity:
Chronic toxicity or long-term toxicity:
K. Toxicity data
Purpose: Provide information on toxicity of chemicals and possible hazard for health, thereby achieving the functions of warning and precaution.

## Slide 43
LD50(50％ Lethal Dose)
  50% lethal dose refers to 50% mortality rate for experimental animals within 14 days after receiving specific dosage (mg/kg) either via feeding or spreading on skin, the lower the value of the indicator the higher the toxicity.
LC50(50％ Lethal Concentration)
  50％ lethal concentration refers to 50% mortality rate for experimental animals within 14 days with a specific time (mostly 1-4 hours) after inhaling gaseous or vaporized chemical at specific density (ppm), the lower the value of the indicator the higher the toxicity.
Toxicity indicator of chemicals

## Slide 44
Ecological toxicity:
Durability and degradability:
Bioaccumulation:
Fluidity in soil:
Other adverse effect:
L. Ecological data
Purpose: Provide data on polluting effect caused by leakage of substance into environment, as reference for environment-protection and waste-disposal workers in handing the situation.

## Slide 45
Waste disposal method：
M. Waste disposal method
Purpose: Offer proper waste disposal method for first-aid responders or environmental-protection workers

## Slide 46
N. Transport data
UN code No.:
UN transport name:
Classification of transport hazard
Kind of packaging:
Oceanic pollutant (yes/no):
Special transport method and notices:
Purpose: Offer noteworthy related regulations on the transport of hazardous substances.

## Slide 47
Applicable laws/regulations：
O. Legal data
Purpose: List laws/regulations related to the substance, to facilitate inquiry by users.

## Slide 48
References |  | 
Production unit |  | Name: Address: Tel. No.:
Producer: | Title: | Name (signature):
Production data |  | 
Note |  | 
Other data
Purpose: Offer data on producer, facilitate inquiry by users.

## Slide 49
Compiled by Li Yi-yang, researcher, Taiwan Occupational Health Association
Edited by Chang Jung Christian University team-Li Yung-hui
Data sources: